# Netmask
A netmask is a mask used to divide an IP address into subnets and specify the number of available host addresses in the subnet.
The netmask consists of a 32-bit sequence on the format 255.255.225.255.
There are three commonly used network classes:
Class	Netmask length	# of networks	Number of hosts	Netmask
Class A	8	126	16777214	255.0.0.0
Class B	16	16382	65534	255.255.0.0
Class C	24	2097150	254	255.255.255.0

The last 0 and 255 in a sequence are always assigned and cannot be used as host addresses.
For example, in 255.255.225.0, 0 is the assigned network address.
In 255.255.255.255, 255 is the assigned IPv4 broadcast address.